# A Mini Project Report on
# EXPERIMENTAL STUDY ON PERFORMANCE OF CONCRETE
Project report submitted in partial fulfillment of the requirement for the award of B.Tech in civil engineering

# BY
# N.Pallavi
# 17H55A0119.
Under the guidance of
NAVED SAYYAD SATTAR
SENIOR TECHNICAL OFFICER
ACC LIMITED
(FORMERLY THE ASSOCIATED CEMENT COMPANIES LIMITED)
        AND
DEPARTMENT OF CIVIL ENGINEERING
CMR COLLEGE OF ENGINEERING AND TECHNOLOGY
KANDLAKOYA.
DEPARTMENT OF CIVIL ENGINEERING

CERTIFICATE

This is to certify that the project entitled “EXPERIMENTAL STUDY ON PERFORMANCE OF CONCRETE” has been carried out by students mentioned below in partial fulfillment of the degree of B.TECH in Civil Engineering from CMR COLLEGE OF ENGINEERING AND TECHNOLOGY during the academic year 2019-2020.

BY
N.Pallavi
17H55A0119.

        Project Guide Examiner Head of the Department

CMR COLLEGE OF COLLEGE OF ENGINEERING & TECHNOLOGY

DECLARATION
I N.Pallavi bearing Roll no. 17H55A0119, here by certify that the project report entitled “EXPERIMENTAL STUDY ON PERFORMANCE OF CONCRETE”, carried out under the guidance of Mr.R.UMA MAHENDRA, Submitted in partial fulfillment of the requirements for the award of the degree of B.TECH in Civil Engineering. This is a record of bonofied work carried out by us and the results embodied in this project report have not been reproduced / copied from any source. The results embodied in this project report have not been submitted to any other university or institute for the award of any other degree or diploma.

        ACKNOWLEDGEMENT

We offer our sincere thanks to external guide Mr.NAVED SAYYAD SATTAR , who was the main impetus behind the endeavor, valuable guidance throughout the project.

 We wish to thank , HOD for creating an excellent academic climate which inspired us to pool up all our intellectual resources to the best of all capacity and made this endeavor a reality.

We owe our gratitude to our principal for his kind attention and valuable guidance throughout the course.

There are many people who have helped us directly or indirectly in the successful completion of the project. We would like to take this opportunity to thank one and all.

        COMPANY OVERVIEW

ACC Limited is one of India's leading manufacturers of cement and ready mix concrete with 17 cement factories, 75 ready mix concrete plants, over 6,700 employees, a vast distribution network of 50,000+ dealers & retailers and a countrywide spread of sales offices.
For over eight decades, ACC has earned the country's trust and goodwill through its valued product portfolio, ethical business practices and governance, focus on sustainable development, and its contributions to society.
Synonymous with cement and enjoying high equity in the Indian market, ACC has consistently set benchmarks in cement and concrete technology since its inception in 1936. From the Bhakra Nangal Dam in 1960 to the Mumbai-Pune Expressway, ACC cement is at the foundation of iconic landmarks across the country.
Anticipating customers’ needs early and being able to serve them with innovative and differentiated products and solutions is a key aspect of its product strategy. ACC’s brand architecture comprises the Gold range and Silver range of products assuring superior quality for general construction as well as for specialised applications and environments. The ready mix concrete product range provides one-stop solutions from basic requirements to high grades of concrete to build the country’s tallest structures.
Sustainability is an integral part of ACC’s business strategy with its Sustainable Development 2030 plan focusing on four broad themes: Climate, Circular Economy, Water & Nature and People & Communities. Its corporate social responsibility efforts benefit local communities across the country by ensuring economic and social progress. ACC’s earliest initiatives in community development date back to the 1940's – long before the term 'corporate social responsibility' was coined.
ACC was among the first Indian companies to include commitment to environmental protection as one of its corporate objectives. Since its inception, the company has continuously explored ways to make its business more planet-friendly and this concern is integrated into all activities of the value chain, from mining to sales to promoting the use of alternative fuels and resources, resulting in one of the lowest carbon footprints in its class.
In 2005, ACC Limited became a part of the reputed Holcim group of Switzerland. In 2015 Holcim Limited and Lafarge SA came together in a merger of equals to form LafargeHolcim – the new world leader in the building materials industry.

        CONTENTS
        PAGE NOS
CHAPTER-I
1. INTRODUCTION
1.1 DEFINITION
1.2 MATERIALS
1.3 PROPORTIONING
1.4 MIXING
1.5 GRADES
CHAPTER-II
2. BIS CODES
CHAPTER-III
3. TESTS ON CONRETE
3.1 GRADATION OF COARSE AGGREGATES
3.2 GRADATION OF FINE AGGREGATES
3.3 SILT CONTENT FOR CRUSHED SAND RIVER SAND
3.4 WATER ABSORBTION FOR FINE AND COARSE AGGREGATE
3.5 DRY LOOSE BULK DENSITY FOR FINE AND COARSE AGGREGATE
3.6 SLUMP TEST SND FLOW TEST FOR CONCRETE
3.7 YIELD TEST FOR CONCRETE
3.8 FLAKINESS AND ELONGATION TEST FOR CONCRETE
3.9 FINENESS OF CEMENT AND FLYASH
3.10 PH TEST FOR WATER AND ADMIXTURE
CHAPTER –IV
4. LIST OF TABLES
CHAPTER-V
5. LIST OF FIGURES
REFERENCE

CHAPTER – 1

1. INTRODUCTION
  1. CONCRETE
Concrete is a construction material composed of cement, fine aggregates (sand) and coarse aggregates mixed with water which hardens with time. Portland cement is the commonly used type of cement for production of concrete. Concrete technology deals with study of properties of concrete and its practical applications.
In a building construction, concrete is used for the construction of foundations, columns, beams, slabs and other load bearing elements.
There are different types of binding material is used other than cement such as lime for lime concrete and bitumen for asphalt concrete which is used for roadconstruction.

1.2 MATERIALS
- CEMENT
- FINE AGGREGATE
- COARSE AGGREGATE
- WATER

CEMENT
A cement is a binder, a substance used in construction that sets and hardens and can bind other materials together. The most important types of cement are used as a component in the production of mortar in masonry, and of concrete, which is a combination of cement and an aggregate to form a strong building material.
Cements used in construction are usually inorganic, often lime based, and can be characterized as being either hydraulic or non-hydraulic, depending upon the ability of the cement to set in the presence of water
Non-hydraulic cement will not set in wet conditions or underwater; rather, it sets as it dries and reacts with carbon dioxide in the air. It is resistant to attack by chemicals after setting.
Hydraulic cements (e.g., Portland cement) set and become adhesive due to a chemical reaction between the dry ingredients and water. The chemical reaction results in mineral hydrates that are not very water-soluble and so are quite durable in water and safe from chemical attack. This allows setting in wet condition or underwater and further protects the hardened material from chemical attack

CEMENT

The following are the types of cement that are in practice:
- Rapid Hardening Cement.
- Quick setting cement.
- Low Heat Cement.
- Sulphates resisting cement.
- Blast Furnace Slag Cement.
- High Alumina Cement.
- White Cement
- Coloured cement

FINE AGGREGATE
Fine aggregate are basically sands won from the land or the marine environment. Fine aggregates generally consist of natural sand or crushed stone with most particles passing through a 9.5mm sieve. As with coarse aggregates these can be from Primary, Secondary or Recycled sources
It is the aggregate most of which passes 4.75 mm IS sieve and contains only so much coarser as is permitted by specification. According to source fine aggregate may be described as:
- Natural Sand– it is the aggregate resulting from the natural disintegration of rock and which has been deposited by streams or glacial agencies
- Crushed Stone Sand– it is the fine aggregate produced by crushing hard stone.
- Crushed Gravel Sand– it is the fine aggregate produced by crushing natural gravE

 COARSE AGGREGATE
## It is the aggregate most of which is retained on 4.75 mm IS sieve and contains only so much finer material as is permitted by specification. According to source, coarse aggregate may be described as:
- Uncrushed Gravel or Stone– it results from natural disintegration of rock
- Crushed Gravel or Stone– it results from crushing of gravel or hard stone.
- Partially Crushed Gravel or Stone– it is a product of the blending of the above two aggregate.
According to size coarse aggregate is described as graded aggregate of its nominal size i.e. 40 mm, 20 mm, 16 mm and 12.5 mm etc. for example a graded aggregate of nominal size 20 mm means an aggregate most of which passes 20 mm IS sieve.
A coarse aggregate which has the sizes of particles mainly belonging to a single sieve size is known as single size aggregate. For example 20 mm single size aggregate mean an aggregate most of which passes 20 mm IS sieve and its major portion is retained on 10 mm IS sieve.

  1. PROPORTIONING
Proportioning of concrete is the process of selecting quantity of cement, sand, coarse aggregate and water in concrete to obtain desired strength and quality.
The proportions of coarse aggregate, cement and water should be such that the resulting concrete has the following properties:
1. When concrete is fresh, it should have enough workability so that it can be placed in the formwork economically.
2. The concrete must possess maximum density or in the other words, it should be strongest and most water-tight.
3. The cost of materials and labour required to form concrete should be minimum.
The determination of the proportions of cement, aggregates and water to obtain the required strengths shall be made as follows:
a) By designing the concrete mix, such concrete shall be called design mix concrete, or
b) By adopting nominal mix, such concrete shall be called nominal mix concrete.
1.4 GRADES OF CONRETE
Grade of concrete is defined as the minimum strength the concrete must posses after 28 days of construction with proper quality control. Grade of concrete is denoted by prefixing M to the desired strength in MPa. For example, for a grade of concrete with 20 MPa strength, it will be denoted by M20, where M stands for Mix.

CHAPTER – 2

2. BIS CODES

S.NO	NAME OF THE TEST	BIS SPECIFICATIONS
1.	ORDINARY PORTLAND CEMENT 43 GRADE-SPECIFICATIONS	IS:8112-2013
2.	ORDINARY PORTLAND CEMENT 53 GRADE-SPECIFICATIONS	IS:12269-2013
3.	SPECIFIC GRAVITY	IS:1199-1959
4.	FINENESS OF CEMENT	IS:4031(PART-I)-1996
5.	CONSISTENCY OF CEMENT	IS:4031(PART-IV)-1988
6.	INITIAL&FINAL SETTING TIME OF CEMENT	IS:4031(PART-V)-1988
7.	SOUNDNESS OF CEMENT a)LE-CHATELIER b)AUTOCLAVE METHOD	IS:4031(PART-III)-1988
8.	COMPRESSIVE STRENGTH OF CEMENT	IS:4031(PART-VI)-1988
9.	PARTICLE SIZE DISTRIBUTION	IS:383:1970 IS:2386(PART-I)-1963
10.	SHAPE TESTS ON AGGREGATES	IS:2386(PART-I)-1963
11.	BULKING OF AGGREGATES	IS:2386(PART-III)-1963
12.	CONCRETE MIX PROPORTIONING –GUIDELINES	IS:10262-2009
13.	SLUMP CONE TEST	IS:1199-1959
14.	COMPACTION FACTOR TEST	IS:1199-1959
15.	VEE-BEE CONSISTOMETER TEST	IS:1199-1959
16.	FLOW TABLE TEST	IS:1199-1959
17.	SLUMP FLOW TEST	…
18.	V FUNNEL (SELF COMPACTING CONCRETE)	…
19.	L BOX (SELF COMPACTING CONCRETE)	…
20.	COMPRESSIVE STRENGTH	IS:516-1959
21.	FLEXURAL STRENGTH	IS:516-1959
22.	SPLITTING TENSILE TEST	IS:516-1959
23.	MODULUS OF ELASTICITY	IS:516-1959
24.	ULTRASONIC PULSE VELOCITY TEST	IS:13311(PART-I)-1992

        CHAPTER – 3

        3.TESTS CONDUCTED ON CONCRETE
3.1 GRADATION OF COARSE AGGREGATES
Objective : To determination of particle size distribution of coarse aggregates by sieving or screening.
 Theory : Grading refers to the determination of the particle-size distribution for aggregate. Grading limits and maximum aggregate size are specified because grading and size affect the amount of aggregate used as well as cement and water requirements, workability, pumpability, and durability of concrete. In general, if the water-cement ratio is chosen correctly, a wide range in grading can be used without a major effect on strength. When gap-graded aggregate are specified, certain particle sizes of aggregate are omitted from the size continuum. Gap-graded aggregate are used to obtain uniform textures in exposed aggregate concrete. Close control of mix proportions is necessary to avoid segregation.
Apparatus : Department of Civil Engineering Sanjay Ghodawat Group of Institutions, Atigre, Kolhapur Test Sieves conforming to IS : 460-1962 Specification of 80 mm, 40 mm, 20 mm, 10 mm, 4.75 mm, 24 Balance, Gauging Trowel, Stop Watch, etc.
 Procedure :
1. The sample shall be brought to an air-dry condition before weighing and sieving. This may be achieved either by drying at room temperature or by heating at a temperature of 100‖ to 110°C. The air-dry sample shall be weighed and sieved successively on the appropriate sieves starting with the largest. Care shall be taken to ensure that the sieves are clean before use.
 2. Each sieve shall be shaken separately over a clean tray until not more than a trace passes, but in any case for a period of not less than two minutes. The shaking shall be done with a varied motion, backward sand forwards, left to right, circular clockwise and anti-clockwise, and with frequent jarring, so that the material is kept moving over the sieve surface in frequently changing directions.
 3. Material shall not be forced through the sieve by hand pressure. Lumps of fine material, if present, may be broken by gentle pressure with fingers against the side of the sieve
 4. On completion of sieving, the material retained on each sieve, together with any material cleaned from the mesh, shall be weighed
### Results of Grain Size Analysis
#### For Coarse Aggregates
        Effective size =……………..micron
        Uniformity coefficient =

SIEVES FOR GRADATION TEST

3.2 GRADATION OF FINE AGGREGATE
Objective: To determine fineness modulus of fine aggregate and classifications based on IS: 383-1970
 Theory: This is the name given to the operation of dividing a sample of aggregate into various fractions each consisting of particles of the same size. The sieve analysis is conducted to determine the particle size distribution in a sample of aggregate, which we call gradation. Many a time, fine aggregates are designated as coarse sand, medium sand and fine sand. These classifications do not give any precise meaning. What the supplier terms as fine sand may be really medium or even coarse sand. To avoid this ambiguity fineness modulus could be used as a yard stick to indicate the fineness of sand. The following limits may be taken as guidance: Fine sand Fineness Modulus: 2.2 - 2.6, Medium sand: F.M. : 2.6 - 2.9, Coarse sand : F.M. : 2.9 - 3.2 Sand having a fineness modulus more than 3.2 will be unsuitable for making satisfactory concrete. 15 Apparatus : Test Sieves conforming to IS : 460-1962 Specification of 4.75 mm, 2.36 mm, 1.18 mm, 600 micron, 300 micron, 150 micron, Balance, Gauging Trowel, Stop Watch, etc.
 Procedure:
1. The sample shall be brought to an air-dry condition before weighing and sieving. The air-dry sample shall be weighed and sieved successively on the appropriate sieves starting with the largest. Care shall be taken to ensure that the sieves are clean before use.
 2. The shaking shall be done with a varied motion, backward sand forwards, left to right, circular clockwise and anti-clockwise, and with frequent jarring, so that the material is kept moving over the sieve surface in frequently changing directions
3. Material shall not be forced through the sieve by hand pressure. Lumps of fine material, if present, may be broken by gentle pressure with fingers against the side of the sieve.
4. Light brushing with a fine camel hair brush may be used on the 150-micron and 75-micron IS Sieves to prevent aggregation of powder and blinding of apertures.
 5. On completion of sieving, the material retained on each sieve, together with any material cleaned from the mesh, shall be weighed
Result:

NOTE:
1. Fineness modulus of a given sample of fine aggregate is …….. That indicates coarse sand/ Medium sand/ Fine sand.
2. ii) The given sample of fine aggregate is belong to Grading Zones I / II / III / IV
Conclusion:
As per above results it confirms to Zone – II.
Reference : IS : 2386 ( Part I ) – 1963,IS: 383-1970

3.3 SILT CONTENT FOR CRUSHED SAND
Objective : To determine silt content in a given sample of fine aggregate by weight method.
Apparatus : 75μ sieve, Fine wire brush, Oven.
Procedure :
1. Take the aggregate Sample min 400gms
2. Dry the aggregates in an oven under 100 5 degree centigrade
3. Weigh the dried aggregates
4. Fill the aggregates in a container filled with water and agitate sample
5. Wash the aggregates over the sieve, until flow of clear water is seen through the sieve
6. Dry the retained aggregate fraction under 110 5 degree centigrade
7. Weigh the dried aggregate & calculate the silt content

Result :
 Weight of sample taken for testing W1 = 520gms
Weight of sample taken for testing W2 = 461gms
Silt Content = (W1-W2)/W1*100
The clay, fine silt and fine dust content of given sample of fine aggregate is found to be 11.35 %

MEASURING JAR

Conclusion : Above Silt content is with IS limits.
Reference : IS : 2386 ( Part II ) - 1963

3.4 WATER ABSORPTION & SPECIFIC GRAVITY FOR FINE AGGREGATE AND COARSE AGGREGATE
I) FINE AGGREGATE : -
Objective : To determine specific gravity & Water absorption of a given sample of fine aggregate.
Apparatus :
Pycnometer, Filter paper , Oven, Weigh balance.
Procedure :
1. Clean the Pycnometer neatly
2. Weigh Pycnometer with Aggregate & Water
3. Weigh Pycnometer with water
4. Weigh SSD Aggregates removed from Pycnometer
5. Dry the SSD aggregate in oven
6. Weigh Oven Dried Aggregates
Calculations :Specific gravity, apparent specific gravity and water absorption shall be calculated as
1. Weight of Pycnometer with aggregate & water A = 1850gms
2. Weight of Pycnometer with water B = 1495gms
3. Weight of Surface dried aggregates removed from Pycnometer C = 505gms
4. Weight of Oven Dried Aggregates D = 481 gms
Apparent Specific Gravity = D/(D-(A-B)) = 2.81
Specific Gravity = D/(C-(A-B)) = 2.46
Water Absorption = (C-D)*100/D = 4.98%

 Result :
i) The Specific Gravity of a given sample of fine aggregate is found to be 2.46
ii) The Water Absorption of a given sample of fine aggregate is found to be 4.98%

I) COARSE AGGREGATE : -
Objective : To determine specific gravity & Water absorption of a given sample of coarse aggregate.
Apparatus :
Glass jar with lid, Filter paper , Oven, 10mm sieve Weigh balance.
Procedure :
1. Take sample which is retained & washed on 10mm sieve
2. Fill the Glass jar with water & aggregate upto top level & weigh it
3. Fill the Glass jar only with water
4. Weigh SSD Aggregates removed from Glass jar
5. Dry the SSD aggregate in oven
6. Weigh Oven Dried Aggregates
Calculations :Specific gravity, apparent specific gravity and water absorption shall be calculated as
1. Weight of Glass jar with aggregate & water A = 3025gms
2. Weight of Glass jar with water B = 2104gms
3. Weight of Surface dried aggregates removed from Glass jar C = 1475gms
4. Weight of Oven Dried Aggregates D = 1468 gms
Apparent Specific Gravity = D/(D-(A-B)) = 2.68
Specific Gravity = D/(C-(A-B)) = 2.64
Water Absorption = (C-D)*100/D = 0.47%

 Result :
i) The Specific Gravity of a given sample of coarse aggregate is found to be 2.64
ii) The Water Absorption of a given sample of coarse aggregate is found to be 0.47%
Reference : IS 2386 ( Part III ) - 1963

3.5 DRY LOOSE BULK DENSITY FOR FINE AND COARSE AGGREGATE
Objective : To determine the Bulk density of Coarse aggrgate & Fine aggregate
Apparatus : Balance, Tamping rod, Cylindrical metal measure of 3 litre capacity ( for fine aggregate ) & 15litre capacity ( for aggregate upto 40mm )
Procedure for Compacted Bulk Density :
1. Measure the volume of the cylindrical metal measure by pouring water into the metal measure and record the volume V in litre
2. Fill the cylindrical metal measure about one-third full with thoroughly mixed aggregate and tamp it 25 times using tamping bar
3. Add another layer of one-third volume of aggregate in the metal measure and give another 25 strokes of tamping bar
4. Finally fill aggregate in the metal measure to over-flowing and tamp it 25 times
5. Remove the surplus aggregate using the tamping rod as a straight edge
6. Determine the weight of the aggregate in the measure and record that weight W in kg
Calculations :
Compacted unit weight of bulk density = W/V
W = Weight of compacted aggregate in cylindrical metal measure, kg
V = Volume of cylindrical metal measure, litre

B. Procedure for Loose Bulk Density
1. Measure the volume of the cylindrical metal measure by pouring water into the metal measure and record the volume V in litre
2. Fill the cylindrical measure to overflowing by means of a shovel or scoop, the aggregate being discharged from a height not exceeding 5 cm above the top of the measure
3. Level the top surface of the aggregate in the metal measure, with a straightedge of tamping bar
4. Determine the weight of the aggregate of the aggregate in the measure and record the weight W in kg
Calculations for Loose Bulk Density :
Loose unit weight or bulk density = W/V
Where,
W = Weight of loose aggregate in cylindrical metal measure, kg
V = Volume of cylindrical metal measure, litre

Result :
The bulk density of C.A is 1514 kg/m3
The bulk density of F.A is 1848 kg/m3
Mention whether the aggregate is
(a) Oven dry,
(b) Saturated and Surface Dry
(c) With a given percentage of moisture